RGA meeting
 ɸ electroproduction analysis : Ks KL channel
20 Jan 2026
M. Ronayette, P. Chatagnon
 rgA - meeting
Mathieu Ronayette
1/26
21 Jan 2026

---
Analysis objective :
- Measurement of the cross section and diferential cross section of the electroproduction of ɸ in the Ks KL channel
π+
e’
e
π-
Ks
q
ɸ
Kl
- Datas : nSidis RG-A inbending and
outbending fall 2018 + spring 2019
p’
p
2/26

---
General informations
Datas :
nSidis Rg-A datas : fall2018 inbending
& outbending
Correction on π+  π- vertex :
Vertex of π+  π- are recalculated with the code
of Veronique Ziegler
 Add some cut on :
→ Distance between vertex of π+  π- < 3.5 cm
→ Distance between vertex Ks and e- :
   1.5 < Dist < 7.0 cm
   because cτKs = 2.68 cm
Cuts :
→ Selection of events with one
 e- , p , π + and π - in the final state. π + π - in FD.
→ Cut on invariant mass of π+ π- with
0.4 < Minv(π+ π-) < 0.6 GeV.
→ Cut on Missing Mass in the reaction
e p → e’ p’ Ks X with 0.4 < MissMass < 0.6 GeV.
3/26

---
Details of cuts on datas
4/26

---
Details of cuts on datas
5/26
rgA - meeting

---
Influence of cuts on datas
6/26
rgA - meeting

---
Influence of cuts on datas
7/26
rgA - meeting

---
Simulation Monte Carlo : ɸ generator
From Proposal to Jeﬀerson Lab PAC39 Exclusive Phi Meson Electroproduction with CLAS12
Branching ratio Ks → π+ π- = 69%
Branching ratio ɸ → Ks Kl = 34%
8/26

---
Simulation Monte Carlo : Validation with ɸ → K+ K-
→ Test my Monte Carlo with a ɸ electroproduction channel wich there is a signal : ɸ → K+ K-
e’
e
K+
q
ɸ
K-
p’
p
Bhawani’s plot
9/26

---
Simulation Monte Carlo : Validation with ɸ → K+ K-
Bhawani’s plot
10/26

---
Simulation Monte Carlo : events reconstructed
11/26
rgA - meeting

---
Simulation Monte Carlo : events reconstructed
12/26

---
Simulation Monte Carlo : comparison with datas
13/26
rgA - meeting

---
Simulation Monte Carlo : comparison with datas
14/26
rgA - meeting

---
Simulation Monte Carlo : comparison with datas
15/26
rgA - meeting

---
Simulation Monte Carlo : comparison with datas
→ MC predicte a problem on acceptance and resolution
16/26

---
Simulation Monte Carlo : comparison generated/reconstructed
Events generated
Events MC reconstructed (after cuts)
17/26

---
Simulation Monte Carlo : comparison generated/reconstructed
Events generated
Events from data (after cuts)
18/26

---
Simulation Monte Carlo : comparison generated/reconstructed
Events generated
(same figure with π+)
19/26
rgA - meeting

---
Simulation Monte Carlo : comparison generated/reconstructed
Events generated
20/26

---
Simulation Monte Carlo : comparison generated/reconstructed
DATA Inbending
21/26
rgA - meeting

---
Simulation Monte Carlo : comparison generated/reconstructed
MC Inbending
22/26
22 Jan 2025

---
Pions in the FT ?
For inbending : events with 1 proton 1 π + and 2 e-
→ one e- in the FD (real e-)
→ one e- in the FT (π – identified like an e-)
For outbending : events with 1 proton 1 π - and 2 e-
→ one e- in the FD (real e-)
→ one e- in the FT (π + identified like an e-)
No correction with veronique zigler code
→ no cuts on vertex
23/26
23 Jan 2026

---
Pions in the FT ?
inbending
24/26

---
Pions in the FT ?
inbending
25/26

---
Conclusion
Conclusion :
We don’t see signal in Ks Kl channel because of problems on pions acceptance and process resolution.
→ For the resolution : we can develop a kinematic fitter ?
→ For the acceptance : we try to detect pions in the FT but we have very poor efficiency (maybe because pions don’t depose energy in the FT calorimeter so they are no detected)
Thanks!
26/26